## Slide 1: Gait Fitness Function Formulation
Shreyas Shandilya
Design of Control System for Quadruped using Central Pattern Generators

## Slide 2: Robot walking Video
Observe the tendency of the robot to topple towards the swinging leg

## Slide 3: Gait Pattern
Pattern in use and problems with it
This Gait Pattern obtained from the formulation in the figure is for a creep walk of the quadruped
The robot walks with this Gait Pattern
But the stability of the quadruped is not maintained
The quadruped tends to topple towards the leg in swing phase

## Slide 4: Architecture
Proposed solution to ensure gait stability
Two methods Proposed to train the gait generation network
  Train the gait generation network end to end using back props and then use RL training for improvement of gait
  Optimise Gait Patterns using fitness function, then train the network end to end using back prop

## Slide 5: Fitness Function
Evaluation Criteria to measure stability, speed and energy consumption
Both the aforementioned training frameworks require a Fitness Function [1]
Fitness Function must measure the following
  Stability Criteria,
  Speed Criteria,
  Energy Efficiency Criteria,
where
  F is the Fitness Value
  , and are integer parameters to account for relative importance of each criteria
  T is the gait period and t is the current time instance

## Slide 6: Stability Criteria
Evaluation of Dynamic and Static Stability of the Quadruped
A Quantitative Measure of quadruped’s dynamic stability
The Criteria must not only take into account current stability but must also anticipate the stability at the next time instance, given the state of motion of the quadruped, like an animal does
Yan Jia, Xiao Luo and others [2] in their paper propose a modified ZMP based stability evaluation criteria
The main idea is that at a certain state, the motion of the robot is considered to be stable if the torque caused by the ground-reaction force can prevent the robot from tumbling around any support boundary

## Slide 7: Stability Criteria
Coordinate Systems used
  There are two coordinate systems of interest-
      The Inertial Coordinate system
The Support Coordinate system
The Support Coordinate has z-axis along the support line AB and x axis perpendicular to the current support plane

## Slide 8: Stability Criteria
Equations for Zero Moment Point
The characteristic equations of ZMP. The inertial force and inertial moment here need to be computed by a dynamic analysis of the quadruped performed later in the report
The force schematic used to calculate the position of ZMP.
Here G is gravity, F is the inertial force on COM C, N is the inertial moment

## Slide 9: Stability Criteria
Virtual Support Plane and Modified Zero Moment Point
The paper assumes that a robot is stable if the current or next set of support feet can provide the moment necessary to prevent the robot from tipping in any direction
A Virtual Support Plane is proposed and it is proposed that if the modified ZMP proposed in the paper lies within this Virtual Support Plane, then the robot motion will be stable
The Proposed Modified ZMP in the paper also includes a velocity term to account for the motion of the quadruped

## Slide 10: Stability Criteria
Calculating the Virtual Support Plane
S is the origin of the support coordinate system on which the ZMP will lie
is the normal vector to the plane
is the normal vector to the place
, and are the normal vectors to the virtual support plane in the inertial frame of reference
is the duration between two adjacent steps and t is the time gap between the current running time and the time point when the previous support line disappeared

## Slide 11: Stability Criteria
Calculation of Modified Zero Moment Point
Zero Moment Point is the point at which the resultant moment on a body is zero
Modified Zero Moment Point should-
  Assess the current stability more efficiently and accurately
  Provide a reference to eliminate undesired velocity during motion planning
can be used to compute 3 measures of dynamic stability
Equations to calculate modified ZMP in support coordinate system. and are the actual and expected velocities in support coordinate system
Rotation Matrix for transformation from support to inertial coordinate system
L and W are the effective length and width respectively of the quadruped

## Slide 12: Stability Criteria
Calculation of the metric
The following three choices for can be calculated using -
Distances between and the boundaries of the virtual-support quadrilateral in the support plane
Angle between the vector pointing from CoM to and the normal vector of the virtual support place
Distance between and the support line
The assumption in the paper that the legs have negligible weight compared to the rest of the body does not hold for the quadruped used
There is a need for evaluation of the repercussions on the concepts introduced

## Slide 13: Speed and Energy Criteria
Calculation of metrics and
Speed Criteria measures the discrepancy between expected and actual speed
  Where is the actual speed and is the distance travelled over period
Energy Criteria measures the energy efficiency of the quadruped
  where is the mass of the quadruped, is the power supplied to the quadruped, is the actual velocity and is the fixed period used in

## Slide 14: Calculating Stability Criteria
Computing ZMP for the available quadruped
The following figure depicts the simplified model of the quadruped.
is the force due to friction acting at the point of contact. This is also the propelling force on the quadruped
is the normal reaction force from the ground
, and are the state of the joints in the four bar linkage in (c)
Simplified model of the leg of the quadruped
Simplified model of the quadruped as seen form the top
Simplified four bar linkage to model the knee of the quadruped

## Slide 15: Calculating Stability Criteria
Relationship between knee joint activation and four bar linkage model angular positions
Of the four angular positions that in the four bar linkage model of the knee joint, the angular position at , and , are known (being the controlled angle). Thus, the other angular positions must also be formulated in terms of and . , , and are intermediate variables.

## Slide 16: Calculating Stability Criteria
Linkage vector in knee joint four bar linkage model
Here is fixed and , the angle between and x-axis is also fixed
, , and are the length of the three linkages given by , , and respectively.
, , and are the length of the three linkages given by , , and respectively.

## Slide 17: Calculating Stability Criteria
Kinematics model of the Knee Joint
The following equations characterise the kinematic model of the knee joint.
These aforementioned relationships arise as the four bar linkage is stationary with respect to and .
These relationships are shorthand for the components of the vectors , , and

## Slide 18: Calculating Stability Criteria
Calculating and
The linkage is fixed
Only rotation with about origin of linkage
Only rotation with about origin of linkage
Only rotation with about origin of linkage

## Slide 19: Calculating Stability Criteria
Calculating and
Solving the above two we get and
Since , we get the following equations.

## Slide 20: Calculating Stability Criteria
Calculating and
The linkage is fixed
Only rotation with about origin of linkage
Only rotation with about origin of linkage
Only rotation with about origin of linkage

## Slide 21: Calculating Stability Criteria
Calculating and
Since , we get the following equations.
Solving the above two we get and

## Slide 22: Calculating Stability Criteria
Dynamic Model of the Available Quadruped
The above two equations depict the dynamics of the quadruped in vector form. Rotation is possible about the and axes, while translation is only possible along the and axes.

## Slide 23: Calculating Stability Criteria
Stance Dynamics
Illustration of all forces acting on the four bar linkage in the knee during stance phase. The segment M1H will be rigid during stance
A simplified model of a leg. and are normal reaction and friction forces respectively

## Slide 24: Calculating Stability Criteria
Stance Dynamics

## Slide 25: Calculating Stability Criteria
Calculating and
and are the friction and normal reaction acting at the points of contact with the ground
To compute these forces the dynamics at the point of contact need to be considered
For a successful walking motion, there must be no slipping at the point of contact
Thus, we need to solve for equilibrium conditions there
where k is the number of legs in contact with the group
This is the condition of no slipping at the point of contact with the ground
The sum of all frictional forces are responsible for the horizontal acceleration of the quadruped

## Slide 26: Calculating Stability Criteria
Calculating Inertial Force and Moment at COM
The Inertial Force and Moment at the COM are given by the following and
Both of these parameters can be calculated by solving of all the equations relating to the dynamics and kinematics of the quadruped
Once the Inertial Force and Moment at the COM are known, the modified ZMP can computed using the method proposed in [2], which can then be used to compute the stability criteria

## Slide 27: 3D model
Quadruped Assembly on Fusion 360
Need for 3D model-
Precise mass of quadruped components
Precise Position of leg COM
Moment of Inertia in Knee four bar linkage
Easier method for URDF model generation
Calculating Joint motion ranges
Fusion 360 can also be used for ML

## Slide 28: 3D model
Quadruped Assembly on Fusion 360

## Slide 29: Solving Quadruped Dynamics
Solving a system of linear equations
The dynamics equations of the quadruped together form a system of 69 equations and 69 variables
is a system of linear equations with being the vector of the unknowns, the matrix of coefficients and the constants
gives the solution to the aforementioned system of linear equations

## Slide 30: Solving Quadruped Dynamics
Solving a system of linear equations
        Some simplifying assumptions were made to formulate the system of linear equations
        A binary factor was introduced for each leg. If there is no contact with the ground at the leg, else there is contact
        If , then .
        If , then
        The resistive force at the hip joint is given by when leg is not in contact with the ground
        Movement is on a flat surface with coefficient of friction
        At least two legs are in contact with the ground at all points of time

## Slide 31: Next Steps
The Quadruped simulation model is complete and the module for solving dynamics and estimating modified ZMP are implemented
Next step is to implement the control architecture and the fitness functions in TensorFlow and integrate the architecture with PyBullet
OpenAI Gym/TensorFlow Agents to be used in conjunction with pybullet for implementing the RL Training Framework
Before the RL pipeline can be implemented up skilling in OpenAI Gym/TensorFlow Agents, RL and Gazebo has to be done

## Slide 32: PyBullet
Collision and Inertia Model of the quadruped
Collisions in the quadruped to be modelled using simple shapes like cylinder, boxed and spheres
There is a need for a simpler collision model as the collision model using meshes requires compute power not currently available
Currently working on the code to control the simulation from a python script

## Slide 33: Reinforcement Learning
Deep Deterministic Policy Gradient

## Slide 34: Reinforcement Learning
Actor Network

## Slide 35: Reinforcement Learning
Actor Network
The action generated by the Actor network will be the joint activations produced by the MLP
The State for DDPG training will consist of the following
    Current joint angle positions
    Current x, y and z position of the centre of mass of the quadruped with respect to the starting point of motion in the current episode
    Desired heading
    Desired Velocity
    Sensory Feedback
    The sensory feedback from the cameras may be encoded using:
    A pre-trained network
    Convolutional layers as a part of the actor network

## Slide 36: Reinforcement Learning
Actor Network
There are two possibilities of how the Actor Network can be modelled:
One time step at a time (action & state are vectors)
The state comprises the CPG previous time step output as well
Less compute required for training
One step at a time (action and/or state are time series)
More compute and memory required to model a recurrent network
Formulation of training will be difficult
Seems to the more realistic model for control
Experiments to be conducted to include , and sequentially to observe how the addition of an additional higher level control parameter impacts CPG output

## Slide 37: Reinforcement Learning
Critic Network
Critic network takes an input the state as well as the action produced by the actor network
The output of the critic network will be the Q value for the current time step
Gradients wrt to the action are computed from the critic network. These gradients are then back propagated through the Actor network to update its parameters

## Slide 38: References
Masuri, Ariel; Medina, Oded; Hacohen, Shlomi; Shvalb, Nir (2020) ‘Gait and Trajectory Optimization by Self-Learning for Quadrupedal Robots with an Active Back Joint’
Jia, Yan; Lua, Xiao; Han, Baoling; Liang, Guanhao; Zhao, Jiaheng; Zhao, Yuting (2018) ‘Stability Criterion for Dynamic Gaits of Quadruped Robot’
Kramer, Oliver; Gong, Daoxiong; Yan, Jie; Zuo, Guoyu (2010) ‘A Review of Gait Optimization Based on Evolutionary Computation’
Timothy P. Lillicrap∗, Jonathan J. Hunt∗, Alexander Pritzel, Nicolas Heess, Tom Erez, Yuval Tassa, David Silver & Daan Wierstra (2016) ‘Continuous Control with Deep Reinforcement Learning’
Bose, Sourabh & Huber, Manfred. (2017). ‘Training Neural Networks with Policy Gradient’
S. Auddy, S. Magg & S. Wermter (2019) "Hierarchical Control for Bipedal Locomotion using Central Pattern Generators and Neural Networks”
Deep Reinforcement Learning