## Slide 1: Quadruped Gait Learning
Shreyas Shandilya
Design of Control System for Quadruped using Central Pattern Generators

## Slide 2: Robot walking Video
Observe the tendency of the robot to topple towards the swinging leg

## Slide 3: Gait Pattern
Pattern in use and problems with it
This Gait Pattern obtained from the formulation in the figure is for a creep walk of the quadruped
The robot walks with this Gait Pattern
But the stability of the quadruped is not maintained
The quadruped tends to topple towards the leg in swing phase

## Slide 4: Architecture
Proposed solution to ensure gait stability
Two methods Proposed to train the gait generation network
  Train the gait generation network end to end using back props and then use RL training for improvement of gait
  Optimise Gait Patterns using fitness function, then train the network end to end using back prop

## Slide 5: Supervised Learning of Gait Pattern
A proportional relationship between fundamental frequency of gait signal and speed of quadruped was established
Using the fundamental frequency as input, it was demonstrated that the proposed network is capable of generating gait patterns
Frequency spectrum of hip joint signal
Hip Joint Signal

## Slide 6: Supervised Learning of Gait Pattern
Gait Pattern for Creep Gait
Model was able to reconstruct gait signal with 100% accuracy for unto 10 different patterns at a time

## Slide 7: Fitness Function
Evaluation Criteria to measure stability, speed and energy consumption
Both the aforementioned training frameworks require a Fitness Function [1]
Fitness Function must measure the following
  Stability Criteria,
  Energy Efficiency Criteria,
where
  F is the Fitness Value
  and are parameters to account for relative importance of each criteria

## Slide 8: Stability Criteria
Evaluation of Dynamic and Static Stability of the Quadruped
A Quantitative Measure of quadruped’s dynamic stability
The Criteria must not only take into account current stability but must also anticipate the stability at the next time instance, given the state of motion of the quadruped, like an animal does
Yan Jia, Xiao Luo and others [2] in their paper propose a modified ZMP based stability evaluation criteria
The main idea is that at a certain state, the motion of the robot is considered to be stable if the torque caused by the ground-reaction force can prevent the robot from tumbling around any support boundary

## Slide 9: Stability Criteria
Coordinate Systems used
  There are two coordinate systems of interest-
      The Inertial Coordinate system
The Support Coordinate system
The Support Coordinate has z-axis along the support line AB and x axis perpendicular to the current support plane

## Slide 10: Stability Criteria
Equations for Zero Moment Point
The characteristic equations of ZMP. The inertial force and inertial moment here need to be computed by a dynamic analysis of the quadruped performed later in the report
The force schematic used to calculate the position of ZMP.
Here G is gravity, F is the inertial force on COM C, N is the inertial moment

## Slide 11: Stability Criteria
Virtual Support Plane and Modified Zero Moment Point
The paper assumes that a robot is stable if the current or next set of support feet can provide the moment necessary to prevent the robot from tipping in any direction
A Virtual Support Plane is proposed and it is proposed that if the modified ZMP proposed in the paper lies within this Virtual Support Plane, then the robot motion will be stable
The Proposed Modified ZMP in the paper also includes a velocity term to account for the motion of the quadruped

## Slide 12: Stability Criteria
Calculating the Virtual Support Plane
S is the origin of the support coordinate system on which the ZMP will lie
is the normal vector to the plane
is the normal vector to the place
, and are the normal vectors to the virtual support plane in the inertial frame of reference
is the duration between two adjacent steps and t is the time gap between the current running time and the time point when the previous support line disappeared

## Slide 13: Stability Criteria
Calculation of Modified Zero Moment Point
Zero Moment Point is the point at which the resultant moment on a body is zero
Modified Zero Moment Point should-
  Assess the current stability more efficiently and accurately
  Provide a reference to eliminate undesired velocity during motion planning
can be used to compute 3 measures of dynamic stability
Equations to calculate modified ZMP in support coordinate system. and are the actual and expected velocities in support coordinate system
Rotation Matrix for transformation from support to inertial coordinate system
L and W are the effective length and width respectively of the quadruped

## Slide 14: Stability Criteria
Calculation of the metric
The following three choices for can be calculated using -
Distances between and the boundaries of the virtual-support quadrilateral in the support plane
Angle between the vector pointing from CoM to and the normal vector of the virtual support place
Distance between and the support line
The assumption in the paper that the legs have negligible weight compared to the rest of the body does not hold for the quadruped used
There is a need for evaluation of the repercussions on the concepts introduced

## Slide 15: Calculating Stability Criteria
Computing ZMP for the available quadruped
The following figure depicts the simplified model of the quadruped.
is the force due to friction acting at the point of contact. This is also the propelling force on the quadruped
is the normal reaction force from the ground
, and are the state of the joints in the four bar linkage in (c)
Simplified model of the leg of the quadruped
Simplified model of the quadruped as seen form the top
Simplified four bar linkage to model the knee of the quadruped

## Slide 16: Calculating Stability Criteria
Relationship between knee joint activation and four bar linkage model angular positions
Of the four angular positions that in the four bar linkage model of the knee joint, the angular position at , and , are known (being the controlled angle). Thus, the other angular positions must also be formulated in terms of and . , , and are intermediate variables.

## Slide 17: Calculating Stability Criteria
Linkage vector in knee joint four bar linkage model
Here is fixed and , the angle between and x-axis is also fixed
, , and are the length of the three linkages given by , , and respectively.
, , and are the length of the three linkages given by , , and respectively.

## Slide 18: Calculating Stability Criteria
Kinematics model of the Knee Joint
The following equations characterise the kinematic model of the knee joint.
These aforementioned relationships arise as the four bar linkage is stationary with respect to and .
These relationships are shorthand for the components of the vectors , , and

## Slide 19: Calculating Stability Criteria
Calculating and
The linkage is fixed
Only rotation with about origin of linkage
Only rotation with about origin of linkage
Only rotation with about origin of linkage

## Slide 20: Calculating Stability Criteria
Calculating and
Solving the above two we get and
Since , we get the following equations.

## Slide 21: Calculating Stability Criteria
Calculating and
The linkage is fixed
Only rotation with about origin of linkage
Only rotation with about origin of linkage
Only rotation with about origin of linkage

## Slide 22: Calculating Stability Criteria
Calculating and
Since , we get the following equations.
Solving the above two we get and

## Slide 23: Calculating Stability Criteria
Dynamic Model of the Available Quadruped
The above two equations depict the dynamics of the quadruped in vector form. Rotation is possible about the and axes, while translation is only possible along the and axes.

## Slide 24: Calculating Stability Criteria
Stance Dynamics
Illustration of all forces acting on the four bar linkage in the knee during stance phase. The segment M1H will be rigid during stance
A simplified model of a leg. and are normal reaction and friction forces respectively

## Slide 25: Calculating Stability Criteria
Stance Dynamics

## Slide 26: Calculating Stability Criteria
Calculating and
and are the friction and normal reaction acting at the points of contact with the ground
To compute these forces the dynamics at the point of contact need to be considered
For a successful walking motion, there must be no slipping at the point of contact
Thus, we need to solve for equilibrium conditions there
where k is the number of legs in contact with the group
This is the condition of no slipping at the point of contact with the ground
The sum of all frictional forces are responsible for the horizontal acceleration of the quadruped

## Slide 27: Calculating Stability Criteria
Calculating Inertial Force and Moment at COM
The Inertial Force at the COM is given by , where is the acceleration of the COM
The Moment at COM is given by , which is calculated by solving the dynamics of the quadruped
Once the Inertial Force and Moment at the COM are known, the modified ZMP can computed using the method proposed in [2], which can then be used to compute the stability criteria

## Slide 28: Solving Quadruped Dynamics
Solving a system of linear equations
The dynamics equations of the quadruped together form a system of 69 equations and 69 variables
is a system of linear equations with being the vector of the unknowns, the matrix of coefficients and the constants
gives the solution to the aforementioned system of linear equations

## Slide 29: Solving Quadruped Dynamics
Solving a system of linear equations
        Some simplifying assumptions were made to formulate the system of linear equations
        A binary factor was introduced for each leg. If there is no contact with the ground at the leg, else there is contact
        If , then .
        If , then
        The resistive force at the hip joint is given by when leg is not in contact with the ground
        Movement is on a flat surface with coefficient of friction
        At least two legs are in contact with the ground at all points of time

## Slide 30: Energy Efficiency Criteria
Calculation of metric
Energy Criteria E measures the energy efficiency of the quadruped
The Criteria is inspired by the objective function used in [9]
There are three aspects of the Energy Efficiency Criteria
  Mean Power
  Mean Power Derivation
  Mean Torque Consumption

## Slide 31: 3D model
Quadruped Assembly on Fusion 360
Need for 3D model-
Precise mass of quadruped components
Precise Position of leg COM
Moment of Inertia in Knee four bar linkage
Easier method for URDF model generation
Calculating Joint motion ranges
Fusion 360 can also be used for ML

## Slide 32: 3D model
Quadruped Assembly on Fusion 360

## Slide 33: PyBullet
Collision and Inertia Model of the quadruped
Collisions in the quadruped to be modelled using simple shapes like cylinder, boxed and spheres
There is a need for a simpler model as the collision model using meshes requires compute power not currently available

## Slide 34: ROS and Gazebo
Due to the limitations of the PyBullet API, the environment for RL had to be changed from PyBullet to ROS and Gazebo
ROS implementation has a much lower simulation to hardware transfer time and Gazebo provides the flexibility of adding sensors into the simulations as needed
Pybullet lacks a forward kinematics module that is needed for computing the future contact positions for the Stability Criteria
MoveIt! Plugin with Gazebo can be very easily be used to get forward as well as inverse kinematics of the quadruped
Gazebo also simplifies Stability Criteria Calculation as it directly provides callbacks for dynamics and kinematics from the physics engine used

## Slide 35: ROS and Gazebo
Simplified Quadruped Model
The initially developed quadruped URDF model required very high computational power for proper simulation, which is not available
A simplified URDF model was developed to simulate the kinematics and dynamics of the quadruped

## Slide 36: Reinforcement Learning
Deep Deterministic Policy Gradient

## Slide 37: Reinforcement Learning
DDPG : Inspiration

## Slide 38: Reinforcement Learning
DDPG : Inspiration
        The proposed DDPG model is inspired by the DDPG for the higher level controller for the biped, proposed in [6]
        The CPG model in [6] is tuned using GA instead of inclusion in the DDPG
        The Actor Network in [6] produces the and which are used to steer the biped by modifying the gait signal according to the following equations:
        The proposed DDPG model combines CPG and MLP training to tune gait generation in a single step
Critic Network in [6]

## Slide 39: Reinforcement Learning
Actor Network
will be the joint activations produced by the network at timestep t
are used only for reward calculation and then discarded
is produced by the CPG at timestep t
State produced by the CPG after timestep t are discarded
Unrolled Actor Network
Such implementation of the Actor Network produces a sliding time window over actions taken by the quadruped around any timestep t

## Slide 40: Reinforcement Learning
Snapshot of Actor Network during inference, at timestep t

## Slide 41: Reinforcement Learning
Actor Network : Motion Encoding Network
Robot State:
Current Joint Angles
Current x, y, z position of the centre of mass of the quadruped in the inertial frame of reference
Motion State:
Desired Turning
Desired Speed along x and y axes
comprises of the following components:

## Slide 42: Reinforcement Learning
Critic Network
Critic is an RNN that iterates over the and
The initial state of the RNN is generated by the intermediate state generator
The last output of the RNN is input to a dense layer to output the predicted Q scores
The Intermediate State Generator combines , and into a single state vector
The RNN cell to be used is LSTM

## Slide 43: Reinforcement Learning
Critic Network : RNN
The Q Score predicted by the RNN takes into account the actions over the time window of actions around a timestep given , and

## Slide 44: Reinforcement Learning
Critic Network : Intermediate State Generator
and are complex numbers
Real and Imaginary parts of and are concatenated and passed to a dense layer
Intermediate Critic State is a combination of , and and is a vector of the same size as an RNN layer

## Slide 45: Reinforcement Learning
Environment
History consists of the action from the previous timesteps
  History is initialised with repetitions of the initial joint positions
  The Environment produces the Robot State and Motion State given
  Reward is produced by the environment given History and Actions
  The Oscillator State produced is passed on unchanged
  is sliced and stacked with to get which is the history for the timestep

## Slide 46: References
Masuri, Ariel; Medina, Oded; Hacohen, Shlomi; Shvalb, Nir (2020) ‘Gait and Trajectory Optimization by Self-Learning for Quadrupedal Robots with an Active Back Joint’
Jia, Yan; Lua, Xiao; Han, Baoling; Liang, Guanhao; Zhao, Jiaheng; Zhao, Yuting (2018) ‘Stability Criterion for Dynamic Gaits of Quadruped Robot’
Kramer, Oliver; Gong, Daoxiong; Yan, Jie; Zuo, Guoyu (2010) ‘A Review of Gait Optimization Based on Evolutionary Computation’
Timothy P. Lillicrap∗, Jonathan J. Hunt∗, Alexander Pritzel, Nicolas Heess, Tom Erez, Yuval Tassa, David Silver & Daan Wierstra (2016) ‘Continuous Control with Deep Reinforcement Learning’
Bose, Sourabh & Huber, Manfred. (2017). ‘Training Neural Networks with Policy Gradient’
S. Auddy, S. Magg & S. Wermter (2019) "Hierarchical Control for Bipedal Locomotion using Central Pattern Generators and Neural Networks”
Doo Re Song, Chuanyu Yang, Christopher McGreavy, Zhibin Li (2018) “Recurrent Deep Deteministic Policy Gradient Method for Bipedal Locomotion on Rough Terrain Challenge”
Deep Reinforcement Learning

## Slide 47: References
Shouwen Fan, Min Sun (2007) “Gait Parameters Optimization and Real-Time Trajectory Planning for Humanoid Robots”